## Slide 1: CSE2312: Computer Organization and Assembly Language Programming
Slide 1: Number Conversion (Integer)

## Slide 2: Decimal/Base-10
10 digits: 0~9
The weight of digit n from the right is 10n
  e.g., the ‘3’ in 5326 is 3*102

## Slide 3: Binary/Base-2 (Unsigned)
2 digits: 0 and 1
The weight is exponent of 2
  Weight of digit n from the right is 2n
  E.g., 10101010 (base-2)
MSb (the most significant bit)
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
LSb (the least significant bit)

## Slide 4: Binary/Base-2 (Unsigned)
2 digits: 0 and 1
The weight is exponent of 2
  Weight of digit n from the right is 2n
  E.g., 10101010 (base-2)
  10101010 (base-2), 0b10101010, 101010102

## Slide 5: Conversion: Binary to Decimal (Unsigned)
Step 1: List the weights of all the digits
Step 2: Multiple digits by their corresponding weights
Step 3: Calculate the sum of all products
Practice: Convert 10101010 (base-2) to decimal
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20

## Slide 6: Ambiguity of type int in C language
Type int is store in binary
C language of different versions use different number of bit for int

## Slide 7: Ambiguity of type int in C language
Type int is store in binary
C language of different versions use different number of bit for int
To avoid ambiguity, this course will use type int with precision (C99)
  uint8_t/uint16_t/uint32_t/uint64_t: unsigned int of 8 bits/16 bits/32 bits/64 bits
  int8_t/int16_t/int32_t/int64_t: signed int of 8 bits/16 bits/32 bits/64 bits

## Slide 8: Range of uintN_t (Unsigned)
Range of uint8_t: 0 (0b00000000) ~255 (0b11111111)
Range of uint16_t: 0 (0b0000000000000000) ~65,535 (0b1111111111111111)
Range of uintN_t: 0 (all 0s) ~ 2N-1 (all 1s)

## Slide 9: Conversion: Decimal to Binary (Unsigned)
Step 0: Check whether the decimal number is within the range
Step 1: List the weights of bits at all the positions
Step 2: Compare the decimal number with weights along the direction from MSb to LSb. If the number is larger than or equal to the weight, subtract the weight from the number, put ‘1’ as the binary digit in this position, and continue with the difference. Otherwise, put ‘0’ and move on to the next weight.
Practice: Convert 53 to uint8_t

## Slide 10: Conversion: Decimal to Binary
53 is within the range of uint8_t (0~255)
53 = 0b00110101
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
53 ≥ 128?
No
0
53 ≥ 64?
No
0
53 ≥ 32?
Yes 53-32=21
1
21 ≥ 16?
Yes 21-16=5
1
5 ≥ 8?
No
0
5 ≥ 4?
Yes 5-4=1
1
1 ≥ 2?
No
0
1 ≥ 1?
Yes
1-1=0
1

## Slide 11: Conversion: Decimal to Binary
Practice: Convert 1000 to uint8_t
Answer: 1000 is larger than 255, it’s impossible

## Slide 12: Hex/Base-16
16 digits: 0~9, A (10), B (11), C(12), D(13), E(14), F(15)
The weight is exponent of 16
  Weight of digit n from the right is 16n
  E.g., the ‘A’ in ABCD (Base-16) stands for 10*163
ABCD (Base-16), 0xABCD, ABCD16

## Slide 13: Conversion: Hex to Decimal
Step 1: List the weights of all the digits
Step 2: Multiple digits by their corresponding weights
Step 3: Calculate the sum of all products
Practice: Convert ABCD (base-16) to decimal
0x (weight)
A B C D
163 162 161 160

## Slide 14: Conversion: Hex to Binary
Solution 1
Step 1: Convert Hex to Decimal
Step 2: Convert Decimal to Binary

## Slide 15: Conversion: Hex to Binary
0x0 = 0 = 0b0000
0x8 = 8 = 0b1000
0xF = 15 = 0b1111
0x8F = 143 = 0b10001111
0x8F8F = 36751 = 0b1000111110001111

## Slide 16: Conversion: Hex to Binary
0x0 = 0 = 0b0000
0x8 = 8 = 0b1000
0xF = 15 = 0b1111
0x8F = 143 = 0b 1000 1111
0x8F8F = 36751 = 0b 1000 1111 1000 1111

## Slide 17: Conversion: Hex to Binary
Convert each hex digit to four binary digit and put them together
Practice: Convert ABCD to binary
  0x ABCD (43981)
 = 0b 1010 1011 1100 1101 (43981)

## Slide 18: Conversion: Binary to Hex
Step 1: Divide the binary digits to segments of four digits
Step 2: Convert every four binary digits to a hex digits, and put them together
Practice: convert 0b1000010010101001 to hex
  0b 1000 0100 1010 1001
= 0x 8 4 A 9

## Slide 19: Conversion: Decimal to Hex
Step 1: Convert Decimal to Binary
Step 2: Convert Binary to Hex

## Slide 20: Homework Examples
Convert the following numbers between bases:
10111011 (base-2) = (base-10)
10111011 (base-2) = (base-16)
What is the range of the following C99 variable types (assuming the processor uses
two’s compliment arithmetic for signed number representation)?
uint8_t uint16_t
to
to

## Slide 21: Binary/Base-2 (signed)
int8_t, int16_t, int32_t, int64_t
2’s complement coding: The weight of the MSb is negative
0 | 1 | 0 | 1 | 0 | 1 0
26 | 25 | 24 | 23 | 22 | 21 20
E.g., 10101010 (base-2)
1
-27
MSb (the most significant bit)
LSb (the least significant bit)

## Slide 22: Conversion: Binary to Decimal (signed)
Step 1: List weights of all digits (MSb is negative)
Step 2: Multiply each digit by its weight
Step 3: Calculate the sum of all products
Practice: Convert 10101010 (int8_t) to decimal

## Slide 23: Why both Unsigned and Signed?
Resource consideration example:
Range of int8_t: 0b10000000 (-128) ~ 0b01111111 (127)
Range of int16_t:
Range of intN_t:
-32768 ~ 32767
−2𝑁−1 ~ 2𝑁−1 − 1
Performance consideration example:
Operations on unsigned integers can be optimized differently by the hardware.
Reliability consideration example:
Using unsigned integers where only non-negative values make sense can help catch logical
errors.

## Slide 24: Sign Bit (MSb)
int8_t numbers and their corresponding decimal
0b0 1 1 1 1 1 1 1
0b0 1 1 1 1 1 1 0
… …
0b0 0 0 0 0 0 0 1
0b0 0 0 0 0 0 0 0
0b1 1 1 1 1 1 1 1
0b1 1 1 1 1 1 1 0
… …
0b1 0 0 0 0 0 0 1
0b1 0 0 0 0 0 0 0
127
126
… …
1
0
-1
-2
… …
-127
-128
MSB is Sign Bit
Sign Bit is 0 for non-negative values Sign Bit is 1 for negative values

## Slide 25: Conversion: Decimal to Binary (signed)
Step 0: Check whether the decimal value is within the range of the type
Step 1: List the weights of bits at all the positions (MSb is negative)
Step 2: If the decimal number is negative, put ‘1’ at the MSb, subtract the weight of the MSb (negative) from the decimal number, and move forward to step 3. Otherwise, put ‘0’ at the MSb, and move forward to step 3.
Step 3: Compare the decimal value yielded from step 2 with the weights of the remaining digits along the direction from the second most significant bit to the LSb. If the decimal value is larger than the weight, put ‘1’ at this digit, subtract the weight from the decimal value, and move on with the difference. Otherwise, move on to the next digit.
Practice: Convert -100 to int8_t

## Slide 26: Conversion: Decimal to Binary (signed)
Practice: Convert -100 to int8_t
-100 = 0b10011100

## Slide 27: Conversion: Decimal to Binary (signed)
Practice: Convert 100 to int8_t
100 = 0b01100100

## Slide 28: Benefits of 2’s Complement Coding
Given a binary number, the computer hardware does not need to know whether
it’s signed or unsigned
With 2’s complement coding, computer can calculate correctly anyway.
0b1 0 0 0 0 0 0 1 + 0b0 0 0 0 0 0 0 1
0b1 0 0 0 0 0 1 0
uint8_t 129 + 1 = 130
uint8_t 130
Int8_t
-127+ 1 = -126
uint8_t
-126

## Slide 29: Benefits of 2’s Complement Coding
Half Adder
2’s Complement Coding simplifies ALU significantly.
Example of a one-bit adder:
Full Adder
Four bits

## Slide 30: Homework Examples
Range of the following C99 variable types assuming the processor uses two’s
compliment arithmetic?
int8_t int16_t
to
to
Binary representation of the C99 variables given below? int8_t x = -40:
int8_t x = -103: